## Slide 1: Feedback Control/Closed Loop Control
Closed-loop control allows for uncertainty in the model as well as noise and disturbances in the system under control
goal
Control
Z=f(x,y)
System
Act
Sense
Disturbance
Z
*Controllers are used in the industry to regulate temperature, pressure, flow rate, chemical composition, speed and practically every other variable for which a measurement exists.
noise
Notes: Given a set of inputs and a goal, a controller makes a calculated decision or action in order to satisfy the goal. This action is then applied to the System, which may be experiencing some external disturbing forces at the same time. Next, within a span of a few milliseconds, sensors monitoring the system will get a set of new input values, to get some feedback on the effects of the action taken. This flow of control repeats, and this is why its called a Closed Loop Control.

## Slide 2: Feedback Control/Closed Loop Control
Closed-loop control allows for uncertainty in the model as well as noise and disturbances in the system under control
goal
Fuzzy Control
Force=f(inputs)
Cart-Pendulum System
Act
Sense
Disturbance
Force
noise
Physics equations
x, x’
Euler’s Method
Balance the pole, keep cart within the boundaries of the platform
Notes: In the simulation, we are using Fuzzy Logic as the controller. We have the cart-pendulum system, and we use a combination of physics equations and Euler’s method to calculate the next state of the world (i.e. the next values for x, x’, ). The goal is simply to keep the pole balanced and keep the cart positioned within the boundaries of the platform.
In the simulation, we are using Fuzzy Logic as the controller. We have the cart-pendulum system, and we use a combination of physics equations and Euler’s method to calculate the next state of the world (i.e. the next values for x, x’, 𝜽,𝜽^′). The goal is simply to keep the pole balanced and the cart within the boundaries of the platform.

## Slide 3: 2 Inputs, 9 rules
Fuzzy Logic Tutorial

## Slide 4: C/C++ version
Fuzzy Logic Engine
Neural Network and Fuzzy Logic Applications in C/C++ (Wiley Professional Computing) by Stephen Welstead

## Slide 5
float inputs[MAX_NO_OF_INPUTS]
Fuzzy Inference System
A function that can execute a complete fuzzy inference system.
We would like a function that feeds on an array of inputs and a complete specification of a fuzzy system, and in turn returns the final crisp output.
fuzzy_system_rec fz
crisp_output = fuzzy_system(inputs, fz);

## Slide 6
// Indices //////////////////////////////////////////////////////////////////////////////////////////////
typedef enum {in_angle, in_distance}; //input indices
//indices of fuzzy sets for angle input
typedef enum {in_negatively_small, in_negatively_medium, in_negatively_large, in_zero, in_positively_small, in_positively_medium, in_positively_large};
//indices of fuzzy sets for distance input
typedef enum {in_near, in_medium, in_far, in_very_far};
//indices for output steering angle
typedef enum {out_ze_turn, out_negatively_very_mild_turn, out_negatively_mild_turn, out_negatively_sharp_turn, out_negatively_very_sharp_turn,
out_positively_very_mild_turn, out_positively_mild_turn, out_positively_sharp_turn, out_positively_very_sharp_turn
};
//indices for output speed
typedef enum {out_very_slow, out_slow, out_medium, out_fast, out_very_fast, out_wicked_fast};
Enumerated data types – for easy indexing
Define enum variables for the linguistic terms.
We would like to refer to the different fuzzy sets and input parameters using descriptive names (e.g. {in_angle, in_position}, {in_negatively_small, in_negatively_large, etc.), instead of numbers whenever we use them.
Add linguistic terms tailored to the problem domain

## Slide 7
Trapezoidal Membership Function
// Trapezoidal Fuzzy Set //////////////////////////////////////////////
struct trapezoid {
trapz_type tp; //type of trapezoid
float a, b, c, d, l_slope, r_slope; //parameters
};
//Trapezoidal membership function types
typedef enum { regular_trapezoid, left_trapezoid, right_trapezoid } trapz_type;
Define a structure for holding the properties of the membership functions to use.
Here we have a structure implementing the trapezoidal membership function.

## Slide 8
Fuzzy Rule
// Fuzzy Rule //////////////////////////////////////////////////////////
typedef struct {
short inp_index[MAX_NO_OF_INPUTS], //input index
inp_fuzzy_set[MAX_NO_OF_INPUTS], //input fuzzy set index
out_fuzzy_set; //output index
} rule;
If ( angle is small) AND (distance is VERY_FAR) Then output is VERY_FAST.
inp_index[0]: in_angle
inp_index[1]: in_distance
out_fuzzy_set
inp_fuzzy_set[0]: in_small
inp_fuzzy_set[1]: in_very_far
Define a structure for holding the components of a fuzzy rule.
Note that we are only storing the indices of the components of a rule.

## Slide 9
Fuzzy System
// The complete Fuzzy System //////////////////////////////////////////////////
typedef struct {
bool allocated;
trapezoid inp_mem_fns [MAX_NO_OF_INPUTS] [MAX_NO_OF_INP_REGIONS];
rule* rules; //note that we need to allocate memory for the rules
int no_of_inputs, //number of inputs
no_of_inp_regions, //number of fuzzy sets associated with each input
no_of_rules, //number of rules
no_of_outputs; //number of fuzzy outputs
float output_values[MAX_NO_OF_OUTPUT_VALUES]; //the values of the outputs
} fuzzy_system_rec;
Define a structure for holding the complete description of a fuzzy inference system.
Here we have a structure implementing a Zero-Order Sugeno Fuzzy inference system.

## Slide 10
If ( angle is small) AND (distance is VERY_FAR) Then output is VERY_FAST.
Defining the Fuzzy Rule
inp_index[0]: in_angle
inp_index[1]: in_distance
out_fuzzy_set
fl->rules[0].inp_fuzzy_set[0] = in_small;
fl->rules[0].inp_fuzzy_set[1] = in_very_far;
fl->rules[0].out_fuzzy_set = out_very_fast;
fl->rules[0].inp_index[0] = in_angle;
fl->rules[0].inp_index[1] = in_distance;
 | NEAR | FAR | VERY FAR
SMALL | Med Speed | Fast Speed | Very Fast
MEDIUM | Slow Speed | Med Speed | Fast Speed
LARGE | Very Slow | Slow Speed | Slow Speed
FAMM
We are only storing the indices in the rule.
fuzzy_system_rec *fl;
//…allocate memory
//…initialise fuzzy parameters
// Fuzzy Rule ////////////////////////////////////////////////
typedef struct {
short inp_index[MAX_NO_OF_INPUTS],
inp_fuzzy_set[MAX_NO_OF_INPUTS],
out_fuzzy_set; //output index
} rule;
How to customise a fuzzy rule?
Here is an example of how we can define a rule with two inputs.

## Slide 11
If ( angle is small) AND (distance is VERY_FAR) Then output is VERY_FAST.
Membership Function
out_fuzzy_set
fl->rules[0].inp_fuzzy_set[0] = in_small;
fl->rules[0].inp_fuzzy_set[1] = in_very_far;
fl->rules[0].out_fuzzy_set = out_very_fast;
fl->rules[i].inp_index[0] = in_angle;
fl->rules[i].inp_index[1] = in_distance;
 | NEAR | FAR | VERY FAR
SMALL | Med Speed | Fast Speed | Very Fast
MEDIUM | Slow Speed | Med Speed | Fast Speed
LARGE | Very Slow | Slow Speed | Slow Speed
fl->inp_mem_fns[variable_index][fuzzy_set]
How to specify which membership function we want to use?
Using the index of the rule input, and index of the fuzzy set, we can easily identify the membership function.
inp_index[0]: in_angle
inp_index[1]: in_distance

## Slide 12
Membership Function data structure
fl->inp_mem_fns[variable_index][fuzzy_set]
fl->rules[0].inp_fuzzy_set[0] = in_small;
fl->rules[0].inp_fuzzy_set[1] = in_very_far;
fl->rules[0].out_fuzzy_set = out_very_fast;
fl->rules[i].inp_index[0] = in_angle;
fl->rules[i].inp_index[1] = in_distance;
inp_mem_fns is a structure containing all the parameters of a
membership function.
trapezoid inp_mem_fns [MAX_NO_OF_INPUTS] [MAX_NO_OF_INP_REGIONS];
Declaration:

## Slide 13
Membership Function Initialisation
fl->inp_mem_fns[in_angle][in_small] =
init_trapz(14.0f, 20.0f, 0.0f, 0.0f, left_trapezoid);
fl->rules[0].inp_fuzzy_set[0] = in_small;
fl->rules[0].inp_fuzzy_set[1] = in_very_far;
fl->rules[0].out_fuzzy_set = out_very_fast;
fl->rules[i].inp_index[0] = in_angle;
fl->rules[i].inp_index[1] = in_distance;
The init_trapz() function is used to initialize inp_mem_fns.
inp_mem_fns is a structure containing all the parameters of a
membership function.

## Slide 14
Calculation of degree of Membership
trapz(inputs[variable_index],fl.inp_mem_fns[variable_index][fuzzy_set])
fl->rules[0].inp_fuzzy_set[0] = in_small;
fl->rules[0].inp_fuzzy_set[1] = in_very_far;
fl->rules[0].out_fuzzy_set = out_very_fast;
fl->rules[i].inp_index[0] = in_angle;
fl->rules[i].inp_index[1] = in_distance;
inp_mem_fns is a structure containing all the parameters of a
membership function.
The trapz function calculates the actual degree of membership of a
given input value in a fuzzy set.
which input
which membership function

## Slide 15
Calculation of degree of Membership
trapz(inputs[variable_index],fl.inp_mem_fns[variable_index][fuzzy_set])
which input
which membership function
float trapz (float x, trapezoid trz) {
switch (trz.tp) {
case left_trapezoid: //opening to the left
if (x <= trz.a)
return 1.0;
if (x >= trz.b)
return 0.0;
/* a < x < b */
return trz.r_slope * (x - trz.b);
case right_trapezoid: //opening to the right
if (x <= trz.a)
return 0.0;
if (x >= trz.b)
return 1.0;
/* a < x < b */
return trz.l_slope * (x - trz.a);
case regular_trapezoid:
if ((x <= trz.a) || (x >= trz.d))
return 0.0;
if ((x >= trz.b) && (x <= trz.c))
return 1.0;
if ((x >= trz.a) && (x <= trz.b))
return trz.l_slope * (x - trz.a);
if ((x >= trz.c) && (x <= trz.d))
return trz.r_slope * (x - trz.d);
} /* End switch */
return 0.0; /* should not get to this point */
} /* End function */

## Slide 16
float fuzzy_system ( float inputs[ ], fuzzy_system_rec fz) {
int i, j;
short variable_index, fuzzy_set;
float sum1 = 0.0f, sum2 = 0.0f, weight;
float m_values[MAX_NO_OF_INPUTS];
for (i = 0; i < fz.no_of_rules; i++) {
for (j = 0; j < fz.no_of_inputs; j++) {
variable_index = fz.rules[i].inp_index[j];
fuzzy_set = fz.rules[i].inp_fuzzy_set[j];
m_values[j] = trapz(inputs[variable_index], fz.inp_mem_fns[variable_index][fuzzy_set]);
} /* end j */
weight = min_of (m_values, fz.no_of_inputs);
sum1 += weight * fz.output_values[ fz.rules[i].out_fuzzy_set ];
sum2 += weight;
} /* end i */
if (fabs(sum2) < TOO_SMALL) { // TOO_SMALL = 1e-6
cout << "\r\nFLPRCS Error: sum2 in fuzzy_system is 0." << endl;
//exit(1);
return 0.0;
}
return (sum1/sum2);
}
Fuzzy System – from fuzzification to defuzzification
which input
which fuzzy set
File: fuzzylogic.cpp

## Slide 17
Inside the function: fuzzy_system ()
for (i = 0;i < fz.no_of_rules;i++) {
for (j = 0;j < fz.no_of_inputs;j++) {
variable_index = fz.rules[i].inp_index[j];
fuzzy_set = fz.rules[i].inp_fuzzy_set[j];
m_values[j] = trapz(inputs[variable_index],
fz.inp_mem_fns[variable_index][fuzzy_set]);
} /* end j */
weight = min_of (m_values,fz.no_of_inputs);
W1 = ?? //user-defined weight - could be any number, positive or negative
W2 = ?? //user-defined weight - could be any number, positive or negative
//numerator
if(i <= 24){ //theta vs. theta_dot
sum1 += weight * (fz.output_values[fz.rules[i].out_fuzzy_set] * W1);
} else { //x vs. x_dot
sum1 += weight * (fz.output_values[fz.rules[i].out_fuzzy_set] * W2);
}
sum2 += weight;
} /* end i */
if (fabs(sum2) < TOO_SMALL) {
cout << "\r\nFLPRCS Error: Sum2 in fuzzy_system is 0. Press key: " << endl;
crispOutput=0.0;
}
crispOutput=(sum1/sum2);
Fuzzy System – modified version
New!
User-defined weights
modifications

## Slide 18: How to use the Fuzzy Logic Engine?

## Slide 19: Fuzzy System Development
fuzzy_system_rec g_fuzzy_system;
File: MyProg.cpp
1. Declare a global variable for the fuzzy system.
#define MAX_NO_OF_INP_REGIONS 7
File: fuzzylogic.h
e.g. 7 Maximum Number of Fuzzy Sets allowed
Define the maximum number of Fuzzy Sets to be used.

## Slide 20: Fuzzy System Development
void initFuzzySystem (fuzzy_system_rec* fl) {
fl->no_of_inputs = 2; //inputs are handled 2 at a time only
fl->no_of_inp_regions = 7; //number of fuzzy sets per input
fl->no_of_rules = 49*2; //number of rules
//----
fl->output_values [out_small_push_left] = -15f; //-15 Newtons
fl->output_values [out_large_push_left] = -100f; //-100 Newtons
//… and so on…
...
fl->rules = new rule [fl->no_of_rules]; //allocate memory for the rules
initFuzzyRules (fl); //initialise the rules
initMembershipFunctions(fl); //initialise the membership //functions
}
2. Initialise the fuzzy system.
File: fuzzylogic.cpp
Notes: Indirection operator (fuzzy_system_rec* fl)
Structure pointer (fl->no_of_inputs = 2; )

## Slide 21: Fuzzy System Development
void initFuzzyRules (fuzzy_system_rec* fl) {
int i;
for (i = 0;i < fl->no_of_rules;i++) {
//(*fl).rules[i].inp_index[0] = in_angle; //alternatively
fl->rules[i].inp_index[0] = in_angle;
fl->rules[i].inp_index[1] = in_angle_dot;
}
fl->rules[0].inp_fuzzy_set[0] = in_negatively_small;
fl->rules[0].inp_fuzzy_set[1] = in_falling_to_left_fast;
fl->rules[0].out_fuzzy_set = out_large_push_left;
// define the other remaining rules next
// and so on...
}
3. Initialise fuzzy rules.
File: fuzzylogic.cpp
Rule #0

## Slide 22: Fuzzy System Development
void initMembershipFunctions ( fuzzy_system_rec* fl ) {
//angle
fl->inp_mem_fns[in_angle][in_negatively_large] = init_trapz(14.0f,20.0f,0.0f,0.0f, left_trapezoid);
fl->inp_mem_fns[in_angle][in_negatively_medium] = init_trapz(14.0f,20.0f,34.0f,40.0f, regular_trapezoid);
//...
fl->inp_mem_fns[in_angle][in_positively_large] = init_trapz (34.0f, 40.0f, 0.0f, 0.0f, right_trapezoid);
//angular velocity
//...
//...
//...
//and so on...
}
4. Initialise membership functions.
File: fuzzylogic.cpp
which fuzzy set

## Slide 23: Inverted Pendulum
void runInvertedPendulum () {
//...
initFuzzySystem(&g_fuzzy_system);
while((GetAsyncKeyState(VK_ESCAPE)) == 0 ) { //while ESC key is not pressed
//...
inputValues [ in_angle ] = prevState.angle;
inputValues[ in_angle_dot ] = prevState.angle_dot;
prevState.Force= fuzzy_system(inputValues, g_fuzzy_system);
//... Calculate new state of the world
newState.angle_double_dot = calc_angular_acceleration(prevState);
//and so on...
cart.setX(newState.x);
rod.setX(newState.x);
rod.setAngle(newState.angle);
cart.draw(); rod.draw();
}
free_fuzzy_rules(&g_fuzzy_system);
//and so on...
}
4. Modify runInvertedPendulum ().
File: MyProg.cpp

## Slide 24: Another Example
Robot Navigation
  Target Pursuit
  Obstacle Avoidance

## Slide 25: Robot navigation
void runGame() {
//...
initFuzzySystemTargetPursuitSpeed(&g_fuzzy_system_pursuit_speed);
// keep running the program until the ESC key is pressed
while((GetAsyncKeyState(VK_ESCAPE)) == 0 ) {
//...
inputValuesPursuitSpeed[ in_angle ] = angleFromTarget;
inputValuesPursuitSpeed[ in_distance ] = distanceFromTarget;
fuzzyPursuitSpeed = fuzzy_system(inputValuesPursuitSpeed, g_fuzzy_system_pursuit_speed);
robot.setSpeed(fuzzyPursuitSpeed);
}
//...
free_fuzzy_rules(&g_fuzzy_system_pursuit_speed);
//and so on...
}
4. Modify runGame().
File: MyProg.cpp

## Slide 26: Robot navigation
void runGame() {
//...
// Target pursuit
fuzzyAngle = fuzzy_system(inputValues, g_fuzzy_system);
newAngle = robot.getAngle() + fuzzyAngle; //adjust robot’s angle
robot.setAngle(newAngle); //update robot’s angle
//and so on...
}
4. Modify runGame().
File: MyProg.cpp

## Slide 27: Robot navigation
5. Calibrate the fuzzy membership functions, fuzzy rules and output fuzzy sets.
If the robot runs in circles, then make the fuzzy outputs smaller.
Check also if the robot is hitting the obstacles. Adjust the parameters until the robot avoids them at different speeds and angles.
File: fuzzylogic.cpp

## Slide 28: Skeleton of Simulation
initPendulumWorld();
initFuzzySystem(&g_fuzzy_system);
while((GetAsyncKeyState(VK_ESCAPE)) == 0 ) {
setactivepage(page);
cleardevice();
senseEnvironment (inputs);
F = fuzzy_system(inputs, g_fuzzy_system);
updateWorld(newWorldState)
drawCartAndRod(newWorldState)
setvisualpage(page);
toggle page //switch to another page
}
void runInvertedPendulum()

## Slide 29: Input and Output
Angle of the rod with respect to the vertical axis (in radians)
Angular velocity of the rod (in radians per second)
Cart position (in meters)
Cart velocity (in meters per second)
OUTPUT
Force to apply (in Newtons)
OUTPUT
INPUTS

## Slide 30: World State
struct WorldStateType{
  void init(){
  x=0.0;
  x_dot=0.0;
  x_double_dot = 0.0;
  angle = 0.0;
  angle_dot = 0.0;
  angle_double_dot = 0.0;
  F = 0.0;
  }
  float x;
  float x_dot;
  float x_double_dot;
  float angle;
  float angle_dot;
  float angle_double_dot;
float const mb=0.1; // mass of broom
float const g=9.8; // pull of gravity
float const m=1.1; // mass of cart & broom
float const l=0.5; // length of broom from //pivot point to centre of mass
float F;
};
WorldStateType prevState, newState;

## Slide 31: Dynamics of the System
float calc_angular_acceleration( const WorldStateType& s){
float a_double_dot=0.0;
a_double_dot = (s.m * s.g * sin(s.angle) - (cos(s.angle)
* (s.F + ((s.mb) * s.l * s.angle_dot * s.angle_dot * sin(s.angle) ) ) ) )
/ ( ((4/3)*s.m * s.l) - (s.mb * s.l * cos(s.angle) * cos(s.angle)));
return a_double_dot;
}
float calc_horizontal_acceleration( const WorldStateType& s){
float x_double_dot=0.0;
x_double_dot = ( s.F + s.mb * s.l * (s.angle_dot * s.angle_dot)* sin(s.angle) - s.angle_double_dot * cos(s.angle) )/ s.m;
return x_double_dot;
}

## Slide 32
void runInvertedPendulum()
//***************************************************************
//Set the initial angle of the pole with respect to the vertical
prevState.angle = 8 * (3.14/180); //initial angle = 8 degrees
initFuzzySystem(&g_fuzzy_system);
while((GetAsyncKeyState(VK_ESCAPE)) == 0 ) {
setactivepage(page);
cleardevice();
drawInvertedPendulumWorld();
//retrieve inputs
inputs[in_theta] = prevState.angle;
inputs[in_theta_dot] = prevState.angle_dot;
inputs[in_x] = prevState.x;
inputs[in_x_dot] = prevState.x_dot;
//1) Enable this only after your fuzzy system has been completed already.
//Remember, you need to define the rules, membership function parameters and rule outputs.
//prevState.F = fuzzy_system(inputs, g_fuzzy_system); //call the fuzzy controller
externalForce=0.0;
externalForce = getKey(); //manual operation
if(externalForce != 0.0)
prevState.F = externalForce;
//---------------------------------------------------------------------------
//continued…
Force to apply.

## Slide 33
void runInvertedPendulum()
//---------------------------------------------------------------------------
// **************************************************************************
// BEGIN - DYNAMICS OF THE SYSTEM
//Calculate the new state of the world
newState.angle_double_dot = calc_angular_acceleration(prevState);
newState.angle_dot = prevState.angle_dot + (h * newState.angle_double_dot);
newState.angle = prevState.angle + (h * newState.angle_dot);
newState.F = prevState.F;
newState.x_double_dot = calc_horizontal_acceleration(prevState);
newState.x_dot = prevState.x_dot + (h * newState.x_double_dot);
newState.x = prevState.x + (h * newState.x_dot);
prevState.x = newState.x;
prevState.angle = newState.angle;
prevState.x_dot = newState.x_dot;
prevState.angle_dot = newState.angle_dot;
prevState.angle_double_dot = newState.angle_double_dot;
prevState.x_double_dot = newState.x_double_dot;
//--------------------------
cart.setX(newState.x);
rod.setX(newState.x);
rod.setAngle(newState.angle);
cart.draw();
rod.draw();
// END - DYNAMICS OF THE SYSTEM
// **************************************************************************
//---------------------------------------------------------------------------
displayInfo(newState);
setvisualpage(page);
page = !page; //switch to another page
}
/2) Enable this only after your fuzzy system has been completed already.
//free_fuzzy_rules(&g_fuzzy_system);
Physics equations and Euler’s method

## Slide 34
int main() {
int graphDriver = 0,graphMode = 0;
initgraph(&graphDriver, &graphMode, "", 1280, 1024); // Start Window
clearDataSet();
try{
runInvertedPendulum();
//3) Enable this only after your fuzzy system has been completed already.
//generateControlSurface_Angle_vs_Angle_Dot();
//4) Enable this only after your fuzzy system has been completed already.
//saveDataToFile("data_angle_vs_angle_dot.txt");
}
catch(...){
cout << "Exception caught!\n";
}
return 0;
}
Control surface generation
int main()

## Slide 35: World Coordinate to Device Coordinate Transformation
for defining the system of coordinates, scaling and zooming-in or out.

## Slide 36: Transformation Equations
WORLD SYSTEM OF COORDINATES
0.0
World System of Coordinates
+x
+y
(Xworld,Yworld)
-x
-2.4 m
2.4 m
3.0 m

## Slide 37: Transformation Equations
WORLD-to-DEVICE COORDINATES
1920 x 1080 pixels
100,000,000 m x 500,000 m
World System of Coordinates
Device System of Coordinates
+x
+y
+x
+y
0
0
(Xworld,Yworld)
(XDevice,YDevice)
COMPUTER SCREEN

## Slide 38: World Boundaries
World System of Coordinates
Device System of Coordinates
SETTING THE BOUNDARIES
Use the upper-left and bottom-right coordinates to set the boundaries
+x
+y
+x
+y
0
0
(Xworld,Yworld)
(XDevice,YDevice)
Top-left: x1, y1
Bottom-right: x2, y2

## Slide 39: Transformation
World System of Coordinates
Device System of Coordinates
Given a world coordinate, what’s the equivalent device coordinate?
+x
+y
+x
+y
0
0
(Xworld,Yworld)
(XDevice,YDevice)

## Slide 40: World-to-Device Coordinates
TRANSFORMATION EQUATIONS
World x-coordinate
For calculating Device_y, replace all x’s with y

## Slide 41: Demonstration
Let’s see a sample solution…
How do we generate the 3D control surface?

## Slide 42: Randomisation
Some Extras...

## Slide 43: Element of Surprise
srand()
Seed for random-number generation
Seed the random-number generator with current time so that the numbers will be different every time we run.
srand( (unsigned)time( NULL ) );
/* Display 10 numbers. */
for( i = 0; i < 10;i++ )
printf( " %6d\n", rand() );

## Slide 44: Element of Surprise
rand()
generates a pseudorandom number - returns int
int randomVal(int min, int max)
{
return (min + (rand() % ((max-min)+1) ));
}
rand() returns a pseudo-random integral number in the range (0 to RAND_MAX-1)

## Slide 45: Element of Surprise
rand()
float randomVal(float min, float max)
{
float r;
r = (float)rand()/RAND_MAX;
r = min + (r*(max-min));
return r;
}
rand() returns a pseudo-random integral number in the range (0 to RAND_MAX)-1

## Slide 46: Time elapsed, wait…
clock()
void wait ( int seconds )
{
clock_t endwait;
endwait = clock () + seconds * CLOCKS_PER_SEC ;
while (clock() < endwait) {}
}
clock_t startTime, elapsedTime;
startTime = clock();
…
...
elapsedTime = (clock() - startTime) / CLOCKS_PER_SEC;

## Slide 47: Keyboard Handling
Function keys, arrow keys, Control and Shift keys, combination of keys

## Slide 48: Keyboard Handling
GetAsyncKeyState
The GetAsyncKeyState function determines whether a key is up or down at the time the function is called, and whether the key was pressed after a previous call to GetAsyncKeyState.
To find other pre-defined constants:
Using google, type the following keywords: msdn vk_shift
Virtual-key code
e.g.
    vk_shift
    vk_control
SHORT GetAsyncKeyState( int vKey ); // vKey - virtual-key code
http://msdn.microsoft.com/en-us/library/ms645540(VS.85).aspx

## Slide 49: Keyboard Handling
GetAsyncKeyState
void moveSprite()
{
if(GetAsyncKeyState(VK_UP) < 0) {
SpriteY = SpriteY + 2; //up
outtext("UP");
}
if(GetAsyncKeyState(VK_DOWN) < 0) {
SpriteY = SpriteY - 2; //down
outtext("DOWN");
….
To find other pre-defined constants:
Using google, type the following keywords: msdn virtual key codes
http://msdn.microsoft.com/en-us/library/ms645540(VS.85).aspx

## Slide 50: Keyboard Handling
GetAsyncKeyState
//general key press event
if(GetAsyncKeyState(VK_SPACE) < 0) {
...
}
//key down event
if((GetAsyncKeyState(VK_SPACE) & 0X0001) ==0X0001){
...
}
//key up event
if((GetAsyncKeyState(VK_SPACE) & 0X8000) ==0X8000){
...
}

## Slide 51
Keyboard Handling
Monitoring the Control and Shift keys:
if(GetAsyncKeyState(VK_CONTROL)<0)
{
ControlFlag =! ControlFlag;
}
bool ControlFlag, ShiftFlag;
if(GetAsyncKeyState(VK_SHIFT)<0)
{
ShiftFlag =! ShiftFlag;
}
For the Tank to Jump to the Right: Control + Shift + Right Arrow key
For the Tank to Jump to the Left: Control + Shift + Left Arrow key

## Slide 52
Keyboard Handling
Possible approach in monitoring key combinations :
if(GetAsyncKeyState(VK_RIGHT)<0)
{
XDir=RIGHT;
if(ShiftFlag)
{
outtext("SHIFT + RIGHT");
ShiftFlag=!ShiftFlag;
}
if(ControlFlag)
{
outtext("CTRL + RIGHT");
if (TankX < getmaxx()-W) TankX += 2;
Angle=Angle-5;
RaiseWheelFlag=TRUE;
ControlFlag=!ControlFlag;
}
…

## Slide 53: End of Presentation
Let me answer some of your questions…
Thanks for listening!
*